## Slide 1: Detecting Abnormal Operation in a Cyclone Preheater
Data preparation · Analysis strategy · Insights
Notes: Introduce the problem: 6 sensors, 5-minute data, about 3.6 years, and the goal of highlighting abnormal periods.

## Slide 2: Data Preparation
01
Timestamp alignment
Mixed month-first / day-first text fixed, so rows sit in true 5-minute order.
02
Sensor error cleaning
Text faults (Not Connect, I/O Timeout) and fake values (0, −185, 1375) set to NaN.
03
Missing data
Gaps left empty, not interpolated; invented data creates fake patterns.
04
Shutdown separation
Kept only hot, fan-pulling hours; dropped 2 h of warm-up after each restart.
WHY
You cannot find “abnormal” until you know “normal.”
A planned shutdown is not a fault; it would swamp the abnormal list.
Correct timestamps keep the sequence physically true.
Notes: Four treatments: fix time order, clean sensor errors, do not invent data, and separate planned shutdowns from running time.

## Slide 3: Analysis Strategy
1
Physics features
Inlet–outlet gas ΔT, pressure drop and draft variability.
2
Hourly medians
Faults last hours to days; minute-level noise is averaged out.
3
Robust z-score
Distance from the rolling median of the last 45 days, scaled by MAD.
4
Persistence
Smoothed and merged; only periods over 12 h are kept.
z = (value − normal) / spread
normal = 45-day rolling median
spread = 1.4826 × MAD
Notes: The key idea: compare each hour with the plant's own local normal. The median and MAD are not distorted by the faults themselves, and the rolling window follows slow drift.

## Slide 4: Where the Abnormal Periods Are
22
abnormal periods
≈1,480 h, about 6% of ~24,000 running hours
Flagged when a feature stays ≥ 5 “normal wiggles” from normal for 12+ hours. The feature out of range longest names the cause.
Chart: 
| Build-up / blockage | Draft instability | Outlet over-temp. | Pressure-drop change
Periods | 14 | 6 | 1 | 1
Build-up Mar–May 2018 (incl. a 12-day blockage), Feb–Mar 2019
Instability Feb–Mar 2017, Oct 2017, Dec 2019
Notes: 22 periods in about 24,000 running hours. Build-up is the largest group, clustered in Mar–May 2018 and Feb–Mar 2019. Draft instability shows up mostly in early 2017.

## Slide 5: Key Findings
~85%
Build-up dominates
Inlet gas stays ~900 °C while the outlet runs cold: hot gas is not flowing through the cyclone.
~2 wks
Slow build, sudden release
ΔT climbs for up to two weeks in 2018, then collapses within hours.
Days
Early warning
ΔT starts rising days before the alarm line; a ΔT trend alert would help.
Missed
Hidden instabilities
Early-2017 draft surges hid behind normal temperatures; temperature-only checks miss them.
Notes: Build-up is about 85% of abnormal hours. The slow-rise, sudden-drop pattern matches a blockage growing and then breaking away. ΔT rising days ahead gives a basis for early warning. Draft instability appears without temperature change.